Tode-RC
Users Guide
Setup and Operation

   http://www.TGit-Tech.com
Firmware Version: 232H
Last Updated: 2023-02-22

# Contents

# Introduction

The Tode Project is a Universal Platform of...

  - User Inter-Face Options
  - Back-plane Models optional Radio & Arduino Micro-Controller
  - Extensions - IO Interfaces, Battery Trays

The Tode System is licensed under the MIT License.
It's hosted on Github.com at: https://github.com/TGit-Tech/Tode-RC

## Specifications

- Remote-Control Tested Distance
  - Test Setup
    - (2) Todes set at Tx Power 30dbm
    - (2) Todes having a 5dbi 20cm Omni antenna
    - Stationary Tode antenna mounted 12ft above ground level
    - Rural Area.
  - Signal can reasonably be used at 2-miles away
  - Signal can be spot gotten (hard to get) at 3-miles away
  - There is no signal past 3-miles
## Menu Structure

Top-Level Menu Structure ( Introduced at Power-ON )

  - Multiple Todes make-up a remote-control-network of Individual Todes.
    - The particular Tode in subject is self-described as This-Tode.

  - Every Tode has (2) Top-Level Display Screens
    - 1st Screen is This-Tode IO-Control Screen ( 1st screen on Power-ON )
    - 2nd Screen is This-Tode SETUP Screen
    - 3rd, 4th, etc.... Screens are Remote Controllable Todes (i.e. Not This-Tode)
1st Screen / This-Todes / IO-Control Screen	2nd Screen / This-Todes / SETUP Screen	3rd , 4th , etc. Screens / Remote-Todes / IO-Control
On initial Power-ON this screen is blank because This-Tode hasn't been configured yet. / Press Right	Where all configuration is done / Press Right	Remote Todes
		On Initial Power-ON the SETUP Screen doesn't change because there are NO other Remote Todes added at this Time.

- Sub-Level Menu Screens ( From This-Todes SETUP Screen )
  - Selecting Radio and will produce Sub-Level Radio Settings.
    GET
  - Selecting Add Device and will produce Add a Device Screen.
    GET
  - Selecting Del Tode and will produce List of Todes.
    GET
  - To Exit a Sub-Level Screen press the button.

# Configure
## Set Name
Enter a Name for This-Tode
SETUP	SETUP, 'Set Name'	SETUP,'Set Name'
Press to the blank [NAME] field. / Press	On 'Set Name' Screen / Press	Text Entry Field highlights (Blue)

Text Entry Field is Red when not selected else Blue when Selected by . / Once Selected (BLUE) Character Position (WHITE) can be Selected by
SETUP / 'Set Name' / Entering a Name	SETUP / 'Set Name' / Saving & Exiting	SETUP

To Edit or Clear a Character Position; Highlight the Text Field (BLUE) and select the character to replace (WHITE) then choose the replacement character press SET. The BLANK character is directly under the “EXIT”.

## Radio Settings
### Requirements
Radio Settings that must be identical for Tode Communication.
SecNet / (Range 01-7F)	Security Code selected by you that prevents unauthorized access to your Tode network.
Frequency / (410 to 441)MHz	The radio frequency (channel) for Tode Communication.

Radio Setting that must be Unique
Address / (Range 0000-FFFE)	A radio address to identify each Tode uniquely decided upon by you.

Other Radio Settings
Tx Power / (21,24,27,30)dBm	Sets the (Tx) Transmitting Power of the Radio. / Lower saves power, Higher transmits farther.
PC Connex / (On -or- Off)	When set to On it ties the radio terminal to the USB Port. / This a special function generally ignored by users.

### Per-Digit Setting
Choose any SecNet Value between 01 to 7F and Set that Value.
SETUP	SETUP / RADIO	SETUP / RADIO (Per-Digit Set)
to select Radio. / Press	to select SecNet / to select Value	Press to change. / Press again to set.

SecNet and Address use Per-Digit Set where each digit is changed at a time. / The WHITE background indicates the selected digit. Use to change the selected digit and to change the digits value. Going beyond the number of select-able digits will exit setting without saving changes.

Choose any *Unique* Address Value for this Tode between 0001 and FFFE and set that Value the same way Per-Digit Set as done to set SecNet.
        - In this example Address is set to 1112.
### Value Setting
Choose any Frequency between 410MHz and 441MHz (default is 433MHz).
  - The chosen frequency must be identical on all Todes expected to communicate with each other.

SETUP / RADIO	SETUP / RADIO	SETUP / RADIO (Value Set)
to Frequency	to select Value	Press to change.

to Increment Value / to Decrement Value	Press to save Value. / to Frequency	again to SETUP

1. Choose the lowest Tx Power level that will sustain communications.

## IO HDW Setting

1. A Tode that has connected devices must know what IO HDW is used to connect the devices. If the Tode will be used only as a hand-held control device, then setting the IO HDW is not needed.
  1. At the time of this writing the only option for connecting devices is a SideIO Plug (SIOST stands for SideIO with Screw Terminals).

SETUP	SETUP	SETUP
to IO HDW	to select Value / (I.e. 'NotSet' in picture)	then or / select SideIO / to set the value

NOTICE: If the IO HDW has not been set before trying to set a device PIN the Tode will notify you with SetHDW as shown below.
## Adding Devices

See 5.1 Section for more information on Device Support and Setup.

SETUP	SETUP / Add Device	This-Tode
or / select Add Device / Press	or / Select Device to Add. / Press	The added device appears as ?NAME? / 0 is the Device Index #

This-Tode / Select Device	Selected Device / =Device Set Name	Selected Device / =Device Setup
select 0?NAME?	Press enter Set Name / for the Device. / Same routine as setting a Tode name.	Re-Select Device. / Press enter Setup / Enter Device specific Setup Settings (Ex. Only)
		Note: OLoOff / Output Low, when Off

## Device Control

Below shows an example of how to change an Output Device’s State.

This can be done on LOCAL (This-Tode) devices or devices on Remote Todes.
To add a Remote Tode see 3.6.Add Tode (Remote)

NOTE: Remote Tode Devices will show a value of ‘?’ until the readings are requesting by pressing .

This-Tode	This-Tode	This-Tode
select RELAY1 / to select Value Value 'Off' / Press	to set a new value. / change Value / to set the value	Once set to 'On' / Relay1 on pin 33 should activate.

## Add Tode (Remote)
- To Remotely Control another Todes Devices.
  - The “Remote” Tode (RC1 with RELAY1:IO-Device used this far)
  - is added to a new Tode (RC2)
- Obtain a 2nd Tode
  - Repeat Steps 3.1.Set Name and Name the 2nd Tode RC2
  - Assign a *Unique* Radio Address to RC2
RC2 Radio Settings	Required	RC1 Radio Settings
	SecNet has to Match. / Address must be different / unique. / Frequency has to Match.
On Tode RC2
	add RC1 by Address	Check for an RC1 “remote” Tode Screen.
select Add Tode	to select Value / to set RC1-Address	Again to load RC1 / RC1 remote Screen

Now the Devices on RC1 can be controlled by RC2. / If the “remote” Tode RC1 failed to show up; try again closer to the unit.

## Deleting

### Deleting Devices
To Delete a Device enter the Device Setup Screen as shown in 3.4.Adding Devices and select Del Device and press .

### Deleting Remote Todes
To Delete a Remote Tode control screen. Select Del Tode on the SETUP menu and then select the Remote Tode by Name on the list and press .

### Factory Reset
Preforming a factory reset deletes the Tode Name and all Devices and Remote Todes. Radio Setting are preserved. To preform this operation…

select Reset???? / Note: The 4-Digit after Reset is the Firmware Version Loaded. / Firmware 231D	to select Value / to set / to set Yes / again to apply.	The Tode will automatically Reboot and the blank Tode screen will show.

# IO Devices

## Common Settings
- Every Device Setup has a Del Device option.
- Every Pin has a corresponding pinMode option.
  - OLoOff = Output Low, when Off – Active High
  - OHiOff = Output High, when Off – Active Low
  - InHigh = Input Pull-Up(High) – Active Low
  - InLow = Input Low – Active High (Default Setting)
## OnOff

On Off Device Setup Screen
Pin	Can be any Pin Selectable
pinMode	See pinMode options in #4.1.Common Settings
Del Device	Select and to delete this device.

## AnaInput

The equation for Value = (Pin-Reading + PreAdd) * (MultNum/MultDen) + Add.
MultDen cannot be 0 so 0 equivocates to 10K (10,000)
On Off Device Setup Screen
Pin	The Pin to read from (must be an ‘A’ pin)
pinMode
PreAdd	1st Add this amount to the Pin reading.
MultNum	2nd Multiply by fraction (Fraction Numerator)
MultDen	(Fraction Denominator)
Add	3rd Add after fraction multiply (i.e. offset value)
Samples	Number of reading to gather and average for value.

## AnaOutput

AnaOutput is the PWM output operation
Pin	Analog Output is Always on PIN #45

## Distance

This is used for Sonic Distance Sensors with a Trigger & Echo Pins.

Distance Device Setup Screen
Trig	The Trigger Pin
	The Trigger Pins pinMode
Echo	The Echo Pin
EchoPMode	Echo Pins pinMode
Samples	Number of Samples to Average for Value

## STSTP3W

This is used for panels with a START and STOP momentary push buttons.

3-Wire On/Off Momentary (3-second) Switch
StartPin	OUTPUT hat triggers to initiate a START button.
StartPMode	StartPin pinMode Setting
StopPin	The Pin that triggers to initiate a STOP button.
StopPMode	StopPin pinMode Setting
Status	INPUT; Pin that determines current state.
StatPMode	Status Pins pinMode
Del Device	Select and to delete this device.

# Automation (Logic)
## SetPoint

Compares an Input Device reading to a User SetPoint and if the Input reading is outside the boundaries (+/- Tolerance) then it sets an Output Device respectively.

For example; A tank of water with a level sensor can maintain it’s water level by switching ON or OFF a pump that feeds the tank.

On Off Device Setup Screen
InputDev	The Device Index to read a value from
InTolernc	The (+/-) tolerance allowed from setpoint
OutTode	The Tode Index of Out Device (optional) or 0-local
OutDev	The Device Index to SET the value on (optional)
LOutSet	SET value on OutDev when Input is < setpoint
HOutSet	SET value on OutDev when Input is > setpoint
	SET value can be ON or OFF
	Or INCR/DECR where Difference between setpoint

## Math

Implements Mathematical Operation on TWO input readings and (Optionally) sends the computed value to an output device if the value breaks tolerance (+/-) boundaries (i.e. Value changes significantly).

On Off Device Setup Screen
In1Dev	The Device Index to read a value from
Operator	(+)(-)(x)(/) plus, minus, times, divide or AVE-average
In2Dev	The Device Index to read a value from
Tolerenc	+/- Change Tolerance before setting Output
OutTode	The Tode Index of Out Device (optional) or 0-local
OutDev	The Device Index to SET the value on (optional)

Note: When OutTode is a Remote Tode; values are only sent every 14s when the In-Value passes +/- Tolerance of the last sent value.

# System

The System menu allows one to do factory resets, enable MQTT, Soft Reset the unit and lookup the firmware version loaded. Pressing the Okay button on the FWver-???? entry causes the Soft Reset.

System Sub-menu
USBSerial	What the Top USB plug is used for (auto-reboots)
Factry RST	Factory Reset
Pub ADiscv	Publish homie MQTT data for Auto-Discovery
SRFWv-????	Soft Reset. Displays current Firmware verson.

- USBSerial allows (3)options
  - NOTICE: Changing the USB-Serial use causes an auto-reboot to occur.
    - None = There is no USB Serial Usage (option for debugging)
    - MQTT = Tode uses USB Serial to communicate with MQTT Server.
    - KBC = Keyboard Control by Serial Input. (For Automated Testing)
        - 8=up	9=Set
      - 4=left, 6=right
        - 2=down	3=Get

- Factry RST erases all Todes and Devices and User-Settings.
- Pub ADiscv publishes ‘homie’ auto-discovery MQTT on-demand.
  - only works when USBSerial=MQTT.

SRFWv preforms a soft (no-erase) reset on-demand and also displays the loaded firmware version. It can be used to reset without power-cycling after making a new setting for USBSerial or any reason to do just a soft-reset.

# MQTT Control

Tode-RC firmware ver.232D+ has support for ‘homieMQTT’ Internet of Things(IoT) control using the Serial plug to connect a Tode to a Raspberry Pi IoT server.

## Tode Setup

In SETUP→System→USBSerial set to ‘MQTT’.
See 6.System for details.

## OpenHab Server Setup

### Openhabian

Download Raspberry-Pi Imager at https://www.raspberrypi.com/software/

When you run it; It'll ask for…
1. Operating System: scroll down and click "Other specific-purpose OS"
  1. Pick & Click "Home assistants and home automation"
  2. Pick & Click "openHAB"
    1. Pick 32-bit as OpenHAB states use 32-bit; works best.
    2. Storage: Choose the Flash-Card Target.

1. Insert Card into Raspberry-Pi and attach an Ethernet Cable
  1. Power the Raspberry Pi and wait a while for boot up process.
  2. Connect to the openHAB UI at http://openhabian:8080
  3. This may take up to 45-Minutes to become available
  4. May have to use MS-DOS">arp -a" command to find it's IP-Address
  5. Enter an administrator Username and Password on Startup.
  6. Connect to the openHAB Log Viewer (frontail): http://openhabian:9001

### Putty

1. Install PuttySSH Terminal on a Home PC.
  1. See: https://putty.org/
  2. Run the Putty terminal
    1. Click on Connection Type: SSH
    2. Enter Host Name: openhabian
    3. click open.
  3. Login
    1. Username: openhabian
    2. Password: openhabian
### MQTT Broker & Client

1. Login to the Server computer (Raspberry Pi) using ‘Putty’ terminal.
  1. Install the MQTT Broker (Mosquitto) on the Raspberry Pi.
    1. See: https://community.openhab.org/t/oh3-mqtt-setup-and-configuration/111494
openhabian:~$ sudo apt install mosquitto
openhabian:~$ sudo systemctl start mosquitto
openhabian:~$ sudo systemctl daemon-reload
openhabian:~$ sudo systemctl enable mosquitto
  1. Also install MQTT Client (mosquitto-clients) on the Raspberry Pi.
Openhabian:~$ sudo apt-get install mosquitto-clients
  1. Visit the above link for enabling outside IP connections if desired.

1. Test the MQTT broker setup with mosquitto-clients.
  1. Login with a 2nd putty terminal and enter
openhabian:~$ mosquitto_sub -v -t 'test/topic'
  1. On the 1st putty terminal send an MQTT publish
openhabian:~$ mosquitto_pub -t 'test/topic' -m 'helloWorld'

verify that the (-m)message ‘helloWorld’ appears on the 2nd terminal.

- Online Instructions for installing an MQTT broker on Raspberry Pi.
  - https://www.openhab.org/addons/bindings/mqtt/

### Serial2MQTT

1. Install serial2mqtt
  1. See: https://github.com/TGit-Tech/Tode-RC-Firmware/tree/main/serial2mqtt_build
openhabian:~$ wget https://raw.githubusercontent.com/TGit-Tech/Tode-RC-Firmware/main/serial2mqtt_build/serial2mqtt.`arch`.zip

openhabian:~$ wget https://raw.githubusercontent.com/TGit-Tech/Tode-RC-Firmware/main/serial2mqtt_build/serial2mqtt.json

openhabian:~$ unzip serial2mqtt.`arch`.zip
openhabian:~$ mv Debug/serial2mqtt.`arch` serial2mqtt

1. Setup crontab to auto-run serial2mqtt at start-up
  1. Start the crontab editor
openhabian:~$ crontab -e
  1. Edit the file adding the following line at the bottom of the file.
@reboot /home/openhabian/serial2mqtt

be sure to save / write changes to file.

1. Check operation
  1. Reboot (Power-Cycle) the Raspberry Pi Server.
  2. Make sure ‘serial2mqtt’ starts after Raspberry Pi reboot
openhabian:~$ ps -x
  PID TTY STAT TIME COMMAND
  347 ? Ss 0:00 /bin/sh -c /home/openhabian/serial2mqtt
  348 ? Sl 0:01 /home/openhabian/serial2mqtt
  1. View the ‘serial2mqtt’ logfile
openhabian:~$ tail -f log.serial2mqtt.0.log
  1. For debugging; you can launch ‘serial2mqtt’ from the command line.
openhabian:~$ ~/serial2mqtt

  1. Attach Tode to the Raspberry Pi by USB cable.
    1. Watch the ‘serial2mqtt’ log file as it connects and publishes data.

### OpenHab

Inside OpenHab you can now add the MQTT binding which also requires an MQTT thing. Once the Tode publishes it’s ‘homie’ MQTT data the first time a ‘tode’ thing will show up in the ‘inbox’ feature.

However; due to OpenHab bugs after a ‘tode’ thing has been added one must instruct the Tode to send the ‘homie’ data a second time. Go to Todes SETUP menu, to ‘System’ menu and select ‘Pub ADiscv’ (stands for Publish Auto-Discovery data) and push the Okay button.

Only after OpenHab has received the ‘homie’ data a second time will the ‘channels’ show up. The rest of OpenHab setup should be instructed in the OpenHab guide.

The Tode publishes MQTT in the form of homie/tode/todename/devicename (gets) + /set for (sets).

It also publishes MQTT in the form of homie/tode/tstodename/tsdevicename where the ‘ts’ prefix stands for timestamped status. ‘ts’ channels are for (gets) only and appends a hexadecimal millisecond timestamp to the gotten value. ( example; ON-2fe3a1). Using OpenHab label card to show this (gotten) value ensures that the sets are preformed correctly. Watch that the timestamp changes after setting a new value.

#### MQTT /get Value Update

Once Widgets are setup to turn things on and off.
Using a Label Card to display “ts” values.

1. Get the UID of the MQTT Broker by clicking the ‘Copy UID’ symbol.
2. Create New script named mqttGet
  1. Use ‘ECMAScript’
  2. actions.get("mqtt","mqtt:broker:58b97f2f4b").publishMQTT("homie/tode/1com6/get","")
  3. Paste your MQTT Broker UID in second get() parameter. And adjust the publish MQTT for the ‘TodeName’ for the /get.
3. Setup the Label Widget to run the ‘GetScript’ when clicked.
  1. Under Action choose ‘Run rule’
  2. Click Rule and select ‘mqttGet’ for the ‘script name’.