Tode Hardware
General Development
Equipment, Tools, Supplies, Procedure and Settings

by TGit-Tech [ http://www.tgit-tech.com ]
Build Version: 212M / Last Updated: 2021-11-06

# Introduction

The Tode System ( Dimmed ones are still a work in progress. Not Available Yet. )

- Tode-RC = Handheld Remote Control Models
  - Model #AMP	Arduino Mega Pro (No RF Module)
  - Model #AMPE32T30	Arduino Mega Pro + Ebyte E32-433T30D (1W/30dbm) RF module
  - Model #AMPE32T20	Arduino Mega Pro + Ebyte E32-433T20D (250mW/20dbm) RF module
  - Model #AMPXBEE	Arduino Mega Pro + Digi XBee RF Module

- Tode-SideIO = Input/Output Stations
  - Model #TSIOST	Tode SideIO with Screw Terminals
  - Model #TSIOAP	Tode SideIO with Aviation Plugs

 Manuals
- User Manual	Operator Instructions including Setup and Wiring
- Hardware Development	How to build the hardware including detailed circuit diagrams
- Firmware Development	How to adjust and create firmware for the Tode

The Tode System is liscensed under the MIT Liscense. It's hosted on Github.com at:
https://github.com/TGit-Tech/Tode-RC

# Workstation $780
## Equipment $530
CNC Mill ( ~ $150 ) / DIY CNC1610 / Equipped with End-Stops and Board-Level Clips / 3.175mm Shank Size	3D Printer ( ~ $150 ) / Anet A8 / Various 3D Printers will work.
Reflow Oven T-962 ( ~ $230) / Infrared IC Heater / 800W

## Tools $130
Solder Iron / With Tiny Tips / Price $40	Dikes / Cutters / Price: $10	Wire Strippers / Price $12	Manification / Price $40

Tweezers Kit / Price: $10	3.5mm Drill Bit / 10Pcs Price $10

## General Supplies $120
CNC Pyramid Bits / 0.2mm Tip 45-deg / 3.175mm shank / Price $10/10pcs	V-Shape CNC Bits / 0.2mmTip 10-deg / Price: $10.00/10pcs	CNC Drill Bits / 0.1 to 1.0mm / 1.0 to 3.0mm / Price$20.00/20pc	Liquid Tin / Price $20
0.031” 60/40 / Rosin-Core Solder / Price $8.00	Lead Solder Paste / Price $16.00	No-Clean / Price: $4.00	Solder Wick / Price $3.50
22 AWG Stranded Colored Wire / Price $20/6-rolls

## Software
https://www.kicad.org/	http://flatcam.org/	bCNC Sender / https://github.com/vlachoudis/bCNC

## CNC Routing a PCB ( Settings & Process )

Printed Circuit Boards can be either ordered from a Custom PCB Manufacturer or created with a CNC Router.

- Custom Manufactured PCB
  - Benefits - Custom PCB manufacturing is by far the better approach.
    - Copper through holes provide better connection
    - A Silk Sscreen for better corrosion resistance
    - Far easier to solder

  - Common Custom Manufacturing Businesses
    - https://oshpark.com/
    - https://jlcpcb.com/
    - https://www.pcbway.com/orderonline.aspx
    - https://www.customcircuitboards.com/
    - https://custompcb.com/

- CNC Routed PCB
  - Benefits
    - Generally cheaper by a couple dollars
    - Instant product (No shipping/manufacturing wait time)
    - Good for designing phases; not good for finished design production.

1. Using the CNC machine shown in Workstation::Equipment
2. Using the 3D Printed 3” x 4” Cu-Clad PCB Holder
3. Using Isolation Bit 45-deg, 0.2mm tip, Diamond Shape
4. Using Flatcam Settings
  1. Cut Z:	-0.05 mm
  2. Travel Z:	1.0 mm
  3. Feed Rate:	45.0 mm/s
  4. Tool Dia:	0.199 mm
  5. Spindle Speed:	2000
  6. Multi-Depth:	Un-Checked
  7. Depth/Pass:	N/A
5. Using bCNC
6. Load PCB onto CNC1610 using PCB holder
7. Load the Trace Isolation Bit ( Suggest 45-deg 0.2mm Tip Diamond Shape )
8. Open bCNC
9. Home the CNC
10. Zero Coordinates	(Under [Control] Press the 'XYZ=0' button)
11. Command G01 X40Y17 F300	(Enter Command at bottom-left press Enter)
12. Zero Coordinates	(Under [Control] Press the 'XYZ=0' button)
13. Manually move bit close but not touching PCB	(Under [Control] bottom-left “Control” Section)
14. Zero Z Coordinate
15. Hook-up Probing Wire to Bit
16. Probe for Board-Level Z=0
  1. Settings → Fast Probe @100, Probe Feed @ 5
  2. Push 'Probe' ribbon button, then under 'Probe' Section click 'Probe' button under 'Goto'.
17. Once the Probe stops and machine goes to 'Idle' Press Z=0.
18. Open File
19. Set Autolevel margins	(Usually ~10x10 Steps)
20. Scan for Autolevel	(Press Ribbon-Bar 'Scan' Button)
21. Probe again and Autolevel Zero
22. Remove Autolevel Probe Wire
23. Start Isolation Routing
24. Preform Isolation Routing
25. Preform Hole Drilling
26. Preform Edge-Cuts
27. Sand & Treat with Liquid Tin