Tode-RC
Using Arduino-Mega Pro and Ebyte E32

Written By: Thomas G (10/2020)
Feel free to use: no strings attached (text content only / images respectfully referenced)
Last Updated: 2020.10.29

# INTRODUCTION

Tpower

- Power Required
  - Mega 2560 – Incoming Voltage 6V to 9V (peek 18Vdc)
    - Output: 5Vdc @ 800mA
    - Output 3Vdc @ 800mA
  - Ebyte E32
    - Input: 3.3V – 5.2Vdc ( Over 5.0Vdc for best preformance; over 5.2V will damage)
    - Data Rate: 0.3Kps to 19.2Kps
    - Transmit Current: 106mA, Receiving Current: 15mA

- The project consists of:
  - Hand-Held “Hand Remote”
  - Pole mounted “Pump Controller”
  - High-Voltage Control “Installation Kit” which consists of components to be added to the pumps electrical panel

- The project is Open Source and its main page Resides at: https://github.com/tgit23/AgIrrigationRemoteControl
  - Releases ( All Finalized Plans, Files and Documentation ) can be downloaded at: https://github.com/tgit23/AgIrrigationRemoteControl/releases
  - This document ( most recent version ) can be seen at: https://tgit23.github.io/AgIrrigationRemoteControl/AgIrrigationPumpRemoteControl.pdf
  - Pre-Built Purchasing options are available – See the projects main page link above

#### Signal Strength ( 2-Miles )

Standard Signal distance is recommended for usage of up to 2-miles

  - Elevated or higher gain antennas can be purchased to extend this range

  - Test Scenario

# Construction

## Costs

- AliExpress order date 20BC
  - Ebyte E32-433T30D LoRa	[ $81.60/10 ]	Savings	[ $159.00/20 ]	= $7.95/ea
  - Mega 2560 PRO Boards	[ $60.07/10 ]	Savings	[ $127.35/20 ]	= $6.37/ea
  - WeAct 1.8-in TFT	[ $2.52/1 ]	Savings	[ $61.51/20 ]	= $3.08/ea
    - TOTAL = $17.40

- 3D Prints
  - 3D Solutech White PLA ( $15.99/ea + tax is $84.75 for (5) 1Kg Rolls = $0.01695/gram )
  - Tode-Handheld-BackCover-E32-433T30D.STL	24g / 2hr 23m	[ $0.10/g ]	= $0.41
  - Tode-CenterCover-Mega2560	18g / 1hr 44m	= $0.31
  - Tode-ScreenKeybCover-TFT1.77.STL	13g / 1hr 17m	= $0.22
  - Tode-WingIO-PS+20ST+2RY	33g / 3hr 6m	= $0.56